#### Headquarters

P.O. Box 3000

Johnstown Castle Estate County Wexford

Ireland

WASTE LICENCE

Licence Register Number: Licensee:

Location of

W0258-O1

Waste Rec Coolatore,

Ferns,

Limited

Coun

Wexford.

HEADQUARTERS

JOHNSTOWN CASTLE ESTATE COUNTY WEXFORD, IRELAND PHONE:     +353-53-9160600

FAx:      +353-53-9160699

WASTE MANAGEMENT ACTS, 1996 TO 2011

WASTE LICENCE

Decision of the ARency, under Section 40(1) of the Waste Managçment Acts. 1996 to 2011

Waste Licence Register No:    W0258-O1

Further to  notice  dated  the 23 day  of February  2012,  the  Agency  in  exercise  of the  powers  conferred on it by the Waste Management Acts, 1996 to 2011, for the reasons hereinafter set out in the attached Decision, grants  this waste licence to Murray  Waste  Recycling,  Coolatore,  Ferns, County  Wexford  to carry  on  the  waste  activities  set  out  below  at  Murray  Waste  Recycling   Limited,   Coolatore,  Ferns,

County  Wexford,  subject to twelve Conditions, as set out in the schedules attached thereto.

A copy of the Decision is attached.

Licensed Waste Activities

Waste Disposal Activities,  in accordance with the Third Schedule of the Waste Management Acts,  1996 to 2011:

Class D 13          Blending or mixing prior to submission to any of the operations numbered D 1 to D 12 (if there is  no other D code appropriate, this can include preliminary operations prior to disposal including pre-processing such as, amongst	others, sorting, crushing, compacting, pelletising, drying, shredding, conditioning or seperating prior to submission to any of the operations numbered Dl to D12).

Class D 14       Repackaging  prior to submission  to any of the operations  numbered  D  1 and D 13.

Class D 15 Storage pending any of the operations numbered D 1 to D 14 (excluding temporary storage (being preliminary storage according to the definition of “collection” in section 5(1), pending collection on the site where the waste is produced.

Waste Recovery Activities,  in accordance with the Fourth Schedule of the Waste Management Acts,  1996 to 2011:

Class R 3 Recycling /reclamation of organic substances which are not used as solvents (including composting and other biological transformation processes),

which includes gasification and pyrolisis using the components as chemicals.

Class R 4	Recycling/reclamation of metals and metal compounds.

Class R 5		Recycling/reclamation  of other inorganic materials, which includes soil cleaning resulting in recovery of the soil and recycling of inorganic construction  materials  [Principal Activityl.

Class R ii	Use of waste obtained from any of the operations numbered R ito R 10. Class R 12	Exchange of waste for submission to any of the operations numbered R I to

R 11 (if there is no other R code appropriate, this can include preliminary operations prior to recovery including pre-processing such as, amongst others, dismantling, sorting, crushing, compacting, pelletising, drying,

shredding, conditioning, repackaging, separating, blending or mixing prior to submission to any of the operations numbered Ri to Ri 1).

Class R 13		Storage of waste pending any of the operations numbered R ito R 12 (excluding temporary storage (being preliminary storage according to the definition of’collection’ in section 5(1)), pending collection, on the site where the waste is produced).

The carrying on of the following activity is refused:

Refused waste disposal activities, in accordance with the Third Schedule of the Waste Management Acts,  1996 to 2011:

Class D 8 Biological treatment not specified elsewhere in this Schedule which results in final compounds or mixtures which are discarded by means of any of  the operations numbered  D  Ito D  12.

Reason: Biological treatment does not take place at the facility.

Sealed by the seal of the Agency on this the 11k” day of July 2012.

PRESENT when the seal of the Agency was affixed hereto:

Dr. Karen Creed, Authorised Person

Environmental Protection A2ency	Licence Reg  No  W0258-OI

### INTRODUCTION

This introduction is not part of the licence and does not purport to be a legal interpretation of the licence.

Murray Waste Recycling Limited has operated a waste recovery facility at Coolatore, Ferns, County Wexford since 2005. The facility was previously regulated under a waste facility permit issued by Wexford County Council (WP/08/23) and authorised to accept 21,000 tonnes of waste per annum. This licence authorises the facility to accept 24,500 tonnes per annum of waste including mixed dry recyclables, recyclables, segregated municipal biowaste, municipal solid waste and construction & demolition waste.

The facility is located in an agricultural area and is bordered on all sides by agricultural land except to the north and northeast where approximately five residential properties are located next to the facility. The closest residential property is less than 25 metres from the facility. A drain runs along the northern boundary of the facility and storm water run-off is discharged here.

There are no process emissions to water or sewer from the facility. Wash down  water  from  the recycling building will be collected in an underground storage tank and tankered off-site to an agreed waste water treatment plant.

The licensee must manage and operate the facility to ensure that the activities do not cause environmental pollution. The  licensee is required to carry out regular environmental monitoring and submit all monitoring results, and a wide range of reports  on the operation and management of the facility, to the Agency.

The licence sets out in detail the conditions under which Murray Waste Recycling Limited, will operate and manage this facility at Coolatore, Ferns, County Wexford.

Introduction

Environmental  Protection Agency	Licence Reg  No. W0258-O1

### Table of Contents

Page No

Glossary of Terms

Decision & Reasons for the Decision	5

Part I Schedule of Activities Licensed	6

Part II Schedule of Activities Refused	7

Part Ill Conditions	8

Condition 1.	Scope	8

Condition 2.	Management of the Facility	9

Condition 3.	Infrastructure and Operation	11

Condition 4.	Interpretation	16

Condition 5.	Emissions	16

Condition  6.	ControL and Monitoring	17

Condition 7.	Resource Use and Energy Efficiency	20

Condition 8.	Materials Handling	20

Condition 9.	Accident Prevention and Emergency Response	22

Condition  10.	Closure, Restoration and Aflercare Management	23

Condition  11.	Notification, Records and Reports	24

Condition  12.	Financial Charges and Provisions	26

SCHEDULE A:	Limitations	28

SCHEDULE  B:	Emission Limits	29

SCHEDULE C:	Control & Monitoring	30

SCHEDULE D:	Specified Engineering Works	32

SCHEDULE F:	Annual Environmental Report	33

Contents

Environmental Protection Agency	Licence Reg. No  W0258-O1

# Glossary of Terms

All terms in this licence should be interpreted in accordance with the definitions in the Environmental Protection Agency Acts 1992 to  2011 / Waste Management  Acts  1996 to 2011, unless otherwise defined in the section.

Adequate  lighting	20 lux measured at ground level.

AER	Annual Environmental  Report.

Agreement	Agreement in writing.

Annually	At approximately twelve-monthly  intervals. Application	The application by the licensee for this licence.

Appropriate	A   waste   management   facility,   duly  authorised   under   relevant   law  and facility	technically  suitable.

Attachment	Any reference to Attachments  in this licence refers to attachments submitted as part of this licence application.

BAT	Best Available Techniques.

Biannually	At approximately six —  monthly intervals.

Biowaste		Biodegradable garden and park waste, food and kitchen waste  from households, restaurants, caterers and retail premises and  comparable  waste from food processing plants.

CEN	Comité	Européen	De	Normalisation	—	European	Committee	for Standardisation.

COD	Chemical Oxygen Demand.

Construction    and	Wastes  that  arise  from  construction,  renovation  and  demolition  activities: demolition  (C&D)	Chapter  17 of the EWC or as otherwise may be agreed.

waste

Containment	A boom that can contain spillages and prevent them from entering drains or boom	watercourses or from further contaminating watercourses.

Daily		During  all  days  of  plant  operation  and,  in  the  case  of  emissions,  when emissions are taking place; with at least one measurement on any one day.

Day	Any 24 hour period.

Daytime	0800 hrs to 2200 hrs.

Environmental Protection Agency	Licence Re No  W0258-O1

dB(A)	Decibels (A weighted).

Documentation	Any  report,  record,  results,  data,  drawing,  proposal,  interpretation  or  other document in written or electronic form which is required by this licence.

Drawing	Any reference to a drawing or drawing number means a drawing or drawing number contained in the application, unless otherwise specified  in  this licence.

Emission  limits	Those limits, including concentration  limits and deposition  rates, established in Schedule B: Emission Limits, of this licence.

EMP	Environmental  Management  Programme.

Environmental	As defined in Directive 2004/35/EC. damage

EPA	Environmental  Protection Agency.

European   Waste	A  harmonised,  non-exhaustive   list  of  wastes  drawn  up  by  the  European Catalogue    (EWC)	Commission  and published  as Commission  Decision 200015321EC  and any subsequent  amendment  published  in  the  Official  Journal  of  the  European

Community.

Facility	Any  site  or  premises  used  for the  purpose  of  the  recovery  of  disposal  of waste.

Ha	Hectare.

Hours of	The hours during which the facility is authorised to be operational. operation

Hours of waste	The hours during which the facility is authorised to accept waste. acceptance

Incident	The following shall constitute as incident for the purposes of this licence:

- an emergency;

- any emission  which  does not comply  with the requirements  of this licence;

- any  exceedance  of  the  daily  duty  capacity  of  the  waste  handling equipment;

- any  trigger  level  specified   in  this  licence  which  is  attained  or exceeded; and,

- any indication that environmental pollution  has, or may have, taken place.

kPa	Kilopascals.

Landfill Directive	Council Directive 1999/3 1/EC.

2

Environmental Protection Agency	Licence Re2 No  W0258.-O1

Leq	Equivalent continuous sound level.

Licence	A Waste Licence issued in accordance with  the  Waste  Management  Acts 1996 to 2011.

Licensee	Murray Waste Recycling Limited, Coolatore, Ferns, County Wexford. Local   Authority	Wexford County Council.

Maintain		Keep in a fit state, including  such regular  inspection,  servicing,  calibration and repair as may be necessary to perform its function adequately.

Monthly	A minimum of 12 times per year, at intervals of approximately one month. Municipal   waste	As defined in Section 5(l) of the Waste Management Acts 1996 to 2011.

Night-time	2200 hrs to 0800 hrs.

Noise-sensitive	Any	dwelling    house,    hotel	or    hostel,	health	building,	educational location  (NSL)	establishment,  place of worship or entertainment, or any other facility or area of high amenity which for its proper enjoyment requires the absence of noise

at nuisance levels.

Oil separator  Device  installed  according to the  International  Standard  IS. EN  858-2:2003 (Separator system for light liquids, (e.g. oil and petrol) — Part 2: Selection of normal size, installation, operation and maintenance).

PRTR	Pollutant Release and Transfer Register. Quarterly	At approximately three — monthly intervals.

Recyclable	Waste types, such as cardboard, batteries, gas cylinders etc, may be recycled. materials

Sample(s)               Unless the context of this licence indicates to the contrary, the term samples shall include measurements taken by electronic instruments.

Sanitary effluent	Wastewater from facility toilet, washroom and canteen facilities. SOP	Standard operating procedure.

Source   segregated	Waste which  is separated  at source; meaning that the waste  is sorted at the waste	point of generation  into a recyclable  fraction(s)  for separate collection  (e.g., paper, metal, glass, plastic, bulk dry recyclables,  biodegradables,  etc.,) and a

residual  fraction.	The  expression   ‘separate  at  source’  shall  be  construed accordingly.

Specified	Those emissions listed in Schedule B: Emission Limits, of this licence. emissions

3

Environmental Protection Agency	Licence Reg  No  W0258-OI

Specified	Engineering works listed in Schedule D: SpecfIed Engineering  Works of this Engineering		licence.

Works

Standard method   A National,  European  or  internationally  recognised  procedure  (e.g.  IS. EN, ISO, CEN, BS or equivalent); or an in-house documented procedure based on the above references; a procedure as detailed in the current edition of “Standard Methods for the Examination of Water and Wastewater” (prepared and published jointly by A.P.H.A., A.W.W.A. & W.E.F.), American Public Health Association, 1015 Fifteenth Street, NW.,  Washington  DC  20005, USA; or an alternative method as may be agreed by the Agency.

Storm water	Rain water run-off from roof and non-process areas.

Temporary		In relation to waste is a period of less than six months as defined in the Waste storage	Management Acts  1996 to 2011.

The Agency		Environmental Protection Agency. TOC	Total organic carbon.

Trade effluent	Trade effluent has the meaning given in the Water Services Act, 2007.

Trigger level	A parameter  value, the achievement or exceedance of which requires certain actions to be taken by the licensee.

Water Services	Wexford County Council. Authority

WEEE	As defined in S.I. No. 340 of 2005.

Weekly		During  all  weeks  of  plant  operation  and,  in  the  case  of  emissions,  when emissions are taking place; with at least one measurement  in any one week.

WWTP	Waste water treatment plant.

4

Environmental Protection Agency	Licence Re2 No  W0258-O1

# Decision  & Reasons for  the Decision

The Environmental Protection Agency is satisfied, on the basis of the information available, that subject to compliance with the conditions of this licence, any emissions from the activity will comply with and will not contravene any of the requirements of Section 40(4) of the Waste Management Acts 1996 to 2011.

In reaching this decision the Environmental Protection Agency has considered the application, supporting documentation and objection received from the applicant and the reports of its inspectors.

5

Environmental Protection Agency	Licence Reg No  W0258-OJ

# Part I Schedule of Activities Licensed

in pursuance of the powers conferred on it by the Waste Management Acts 1996 to 2011, the Environmental Protection Agency (the Agency) under Section 40(1) of the said Acts, hereby grants this Waste Licence to Murray Waste Recycling Limited, Coolatore, Ferns, County Wexford to carry on the waste activities listed below at Coolatore, Ferns, County Wexford subject to conditions, with the reasons therefor and the associated schedules attached thereto set out in the licence.

Licensed Waste Disposal Activities, in accordance with the Third Schedule of the Waste Management Acts 1996 to 2011

Class D 13            Blending or mixing prior to submission to any of the operations numbered D 1 to D 12 (if there is no other D code appropriate, this can include preliminary operations prior to disposal including pre-processing such as, amongst others, sorting, crushing,  compacting,  pelletising,  drying, shredding, conditioning or seperating prior to submission to any of the operations numbered Di to D12).

Class D  14		Repackaging  prior  to  submission  to  any  of  the  operations  numbered   D   1 and D  13.

Class D 15 Storage pending any of the operations numbered D  I  to D  14 (excluding temporary storage (being preliminary storage according to the definition of “collection” in section 5(1), pending collection on the site where the waste is produced.

Licensed Waste Recovery Activities, in accordance with the Fourth Schedule of the

Waste Management Acts 1996 to 2011

Class R 3		Recycling /reclamation  of organic substances which are not used as solvents (including composting and other biological transformation  processes),

which includes gasification and pyrolisis using the components as chemicals.

Class R 4	Recycling/reclamation  of metals and metal compounds.

Class R 5		Recycling/reclamation  of other inorganic materials, which includes soil cleaning resulting in recovery of the soil and recycling of inorganic construction  materials  [Principal Activityj.

Class R II    Use of waste obtained from any of the operations numbered R Ito R 10. Class R 12       Exchange of waste for submission to any of the operations numbered R ito

R 11 (if there is no other R code appropriate, this can include preliminary operations prior to recovery including pre-processing such as, amongst others, dismantling, sorting, crushing, compacting, pelletising, drying,

shredding, conditioning, repackaging, separating, blending or mixing prior

to submission to any of the operations numbered RI to Rl 1).

Class R 13		Storage of waste pending any of the operations numbered R ito R 12 (excluding temporary storage (being preliminary  storage according to the definition of’collection’ in section 5(1)), pending collection, on the site where the waste is produced).

6

(j2

Environmental Protection Agency	Licence Re No  W0258-O1

# Part II Schedule of Activities Refused

The Environmental  Protection  Agency  (the Agency),  under  Section 40(1) of the said  Acts, hereby refuses the following class of activity.

Refused waste recovery activities, in accordance with the Third Schedule of the Waste Management Acts 1996 to 2011

Class D 8             Biological treatment not specified elsewhere in this Schedule which results in final compounds or mixtures which are discarded by means of any of the operations numbered D I to D 12.

Reason: Biological treatment does not take place at the facility.

7

Environmental Protection Aciencv	Licence Re No  W0258-O1

# Part III Conditions

## Condition 1.	Scope

  - Waste activities at this facility shall be restricted to those listed and described in Part I Schedule ofActivities Licensed, and shall be as set out in the licence application or as modified  under Condition 1.4 of this licence and subject to the conditions of this licence.

  - Activities at this facility shall be limited as set out in ScheduleA: Limitations, of this licence.

  - For the purposes of this licence, the facility is the area of land outlined in red on Drawing No. Ce07-253-01-206 Revision A of the application. Any reference in this licence to “facility” shall mean the area thus outlined in red. The licensed activities shall be carried on only within the area outlined.

  - No alteration to, or reconstruction in respect of, the activity, or any part thereof, that would, or is likely to, result in

    - a material change or increase in:

      - the nature or quantity of any emission;

      - the abatementltreatment  or recovery systems;

      - the range of processes to be carried out;

      - the   fuels,   raw   materials,    intermediates,    products   or   wastes generated, or

    - any changes in:

      - site	management,	infrastructure	or	control	with	adverse environmental  significance;

shall be carried out or commenced without prior notice to, and without the agreement of, the Agency.

  - The facility shall be controlled, operated and maintained, and emissions shall take place as set out in the licence. All programmes required to be carried out under the terms of this licence become part of this licence.

  - This licence is for purposes of waste licensing under the  Waste Management Acts 1996 to 2011 only and nothing in this licence shall be construed as negating the licensee’s statutory obligations, or requirements under any other enactments or regulations.

  - Waste Acceptance Flours and Hours of Operation

    - With the exception of emergencies or as may be agreed by the Agency, the waste facility shall be operated only between the hours of 0630 and 2100 Monday to Saturday inclusive. During night-time hours, all operations shall take place indoors.

    - With the exception of emergencies or as may be agreed by  the  Agency, waste shall be accepted at or dispatched from the facility only between the hours of 0800 and 2000 Monday to Saturday inclusive.

    - The facility shall not operate or accept/dispatch waste on Sundays  or  on Public Holidays unless agreed by the Agency.

Reason:	To clarify the scope of this licence.

8

Environmental Protection Agency	Licence Reg  No  W0258-OI

## Condition 2.	Management of the Facility

  - Facility Management

    - The licensee shall employ a suitable qualified and experienced facility manager who shall be designated as the person in charge. The facility manager or a nominated, suitably qualified and experienced deputy shall be present on the facility at all times during its operation or as otherwise required by the Agency.

    - The licensee shall ensure that personnel performing  specifically  assigned tasks shall be qualified  on the basis  of appropriate education, training and experience as required and shall be aware of the requirements of this licence.	In addition, the facility manager and his/her deputy shall successfully complete a FAS waste management training programme or a Certificate in Compost Facility Operation or equivalent agreed by the Agency.

  - Environmental  Management System (EMS)

    - The licensee shall establish and maintain an Environmental Management System (EMS) within six months of the date of grant of this licence. The EMS shall be updated on an annual basis.

    - The EMS shall include, as a minimum, the following elements:

      - Management and Reporting Structure.

      - Schedule of Environmental  Objectives and Targets

The	licensee shall prepare and maintain a Schedule of Environmental Objectives and Targets. The schedule shall as  a minimum provide for a review of all operations and processes, including an evaluation of practicable options for energy and resource efficiency, the use of cleaner technology, and the prevention, reduction and  minimisation  of  waste   for  disposal. The schedule shall include time frames for the achievement of set targets and shall address a five year period as a minimum.  In relation  to  waste  recovery   the   schedule   shall   include   an initial waste recovery target of waste throughput, as well as time frames for achieving higher recovery targets. As a minimum this shall include  specific objectives  for the  control  and  minimisation as well as an annual review of the dust and noise nuisance potential of the site activities. The schedule shall be reviewed annually and amendments thereto notified to the Agency for agreement as part of the Annual Environmental  Report (AER).

      - Environmental  Management  Programme (EMP)

The licensee shall, not later than six months from the date of grant of this licence, submit to the Agency for agreement an EMP, including a time schedule, for achieving the Environmental Objectives and Targets prepared under Condition 2.2.2.2. Once agreed the EMP shall be established and maintained by the licensee.  It shall include:

        - designation of responsibility  for targets;

        - the means by which they may be achieved;

        - the time within which they may be achieved.

The EMP shall be reviewed annually and amendments thereto notified to the Agency for agreement as part of the Annual Environmental Report (AER).

9

Environmental Protection Aencv	Licence Re No. W0258-Oi

A report on the programme, including the success in  meeting agreed targets, shall be prepared and submitted to the Agency as part of the AER. Such reports shall be retained on-site for a period of not less than seven years and shall be available for inspection by authorised persons of the Agency.

      - Documentation

- The licensee shall establish and  maintain  an environmental management documentation system which shall be to the satisfaction of the Agency.

- The licensee shall issue a copy of this licence to all relevant personnel whose duties relate to any condition of this licence.

      - Corrective Action

The licensee shall establish procedures to ensure that corrective action is taken should the specified requirements of this licence not be fulfilled. The responsibility and authority for persons initiating further investigation and corrective action in the  event  of  a reported non-conformity with this licence shall be defined.

      - Awareness and Training

The licensee shall  establish  and  maintain  procedures  for identifying training needs, and  for providing  appropriate training, for all personnel whose work can have a significant effect upon the environment. Appropriate records of training shall be maintained.

      - Communications  Programme

The licensee shall establish and maintain a Public Awareness and Communications Programme to ensure that members of the public can obtain information at the facility, at all reasonable times, concerning the environmental performance  of the facility.

      - Maintenance  Programme

The licensee shall establish and maintain a programme for maintenance of all plant and equipment based on the instructions issued by the manufacturer/supplier or installer of the equipment. Appropriate record keeping and diagnostic  testing  shall  support this maintenance programme. The licensee shall clearly allocate responsibility for the planning, management and execution of all aspects of this programme to appropriate personnel  (see Condition

2.1 above).

      - Efficient Process Control

The licensee shall establish and maintain a programme to ensure there is adequate control of processes under all modes of operation. The programme shall identify the key indicator parameters for process control performance, as well as identifying methods for measuring and controlling these parameters. Abnormal process operating conditions shall be documented, and analysed to identify any necessary corrective action.

Reason:		To make pro visionfor  management of the activity on a planned  basis having regard to the desirability of ongoing assessment, recording and reporting of matters affecting the environment.

10

Environmental Protection A.gency	Licence Re No  W0258-O1

## Condition 3.	Infrastructure  and Operation

  - Specified Engineering Works

3. 1.1 The licensee shall submit proposals for all Specified Engineering Works, as defined in Schedule D: Specfied Engineering Works, of this licence, to the Agency for its agreement at least two months in advance of the  intended date of commencement of any such works.  No such works shall be carried out without the prior agreement of the Agency.

    - All specified engineering works shall be  supervised  by  a  competent person(s) and  that person, or persons, shall  be present at all times during which relevant works are being undertaken.

    - Following the completion of all specified engineering works,  the  licensee shall complete a construction quality assurance validation. The validation report shall be made available to the Agency on request. The report shall, as appropriate, include the following information:

      - A description of the works;

      - As-built drawings of the works;

      - Any other information requested in writing by the Agency.

  - Facility Security

    - Security and stockproof fencing and gates shall be installed and maintained.

The base of the fencing shall be set in the ground. Subject to the implementation of the restoration and aftercare plan and to the agreement of the Agency, the requirement for such site security may be removed.

    - The licensee shall install a CCTV system which records all truck movement into and out of the facility; the CCTV system shall be operated at all times and copies of recording kept on site and made available to the Agency on request.

    - Gates shall be locked shut when the facility is unsupervised.

    - The licensee shall remedy any defect in the gates and/or fencing as follows:

      - A temporary repair shall be made by the end of the working day; and

      - A repair  to the standard  of the original  gates and/or fencing shall be undertaken within three working days.

  - Facility Roads and Site Surfaces

    - Effective site roads shall be provided  and maintained to ensure the safe and nuisance-free movement of vehicles within the facility.

    - The licensee shall provide and maintain an impermeable concrete surface in the areas of the facility shown on Drawing No. Ce07-253-0l-206 Revision A; the surfaces shall be concreted and constructed to British Standard 8110 or an alternative as agreed by the Agency. The licensee shall remedy any defect in concrete surfaces within five working days.

  - Facility Office

    - The licensee shall provide and maintain an office at the facility. The office shall be constructed and maintained in a manner suitable for the processing and storing of documentation.

    - The licensee shall provide and maintain a working telephone and a method for electronic transfer of information at the facility.

11

Environmental Protection Agency	Licence Rg. No  W0258-O1

  - Facility Notice Board

    - The licensee shall, within one month of the date  of grant of this  licence, provide a Facility Notice Board on the facility so that it is legible to persons outside the main entrance to the facility. The minimum dimensions of the board shall be 1200 mm by 750 mm. The notice board shall be maintained thereafter.

    - The board shall clearly show:

      - the name and telephone number of the facility;

      - the normal hours of opening;

      - the name of the licence holder;

      - an emergency out of hours contact telephone number;

      - the licence reference number; and

      - where  environmental  information  relating  to  the  facility  can  be obtained.

    - A plan of the facility clearly identifying the location of each storage and treatment area shall be displayed as close as is possible to the entrance to the facility. The plan shall be displayed on a durable material  such that is legible at all times. The plan shall be replaced as material changes to the facility are made.

  - Waste Inspection and Quarantine Areas

    - A Waste Inspection Area and a Waste Quarantine Area shall be provided and maintained at the facility.

    - These areas shall be constructed  and maintained in a manner suitable, and be of a size appropriate, for the inspection of waste and subsequent quarantine if required. The waste inspection area and the waste quarantine area shall be clearly identified and segregated from each other.

    - Drainage from these areas shall be directed to the “drain to collect leachate/wash water” shown on Drawing No. Ce07-253-0l-206  Revision A.

  - Weighbridge and Wheel Cleaners

    - The licensee shall provide and maintain a weighbridge and  a  means  of wheel cleaning at the facility.

    - The wheel cleaners shall be used by all vehicles leaving the facility as required to ensure that no trade effluentlstorm water or waste is carried off- site. All water from the wheel cleaning area shall be directed to the trade effluent drainage network.

    - The wheel-wash  shall be inspected on a daily basis and drained as required.

Silt,  stones  and  other  accumulated  material  shall  be  removed  as required from the wheel-wash and disposed of appropriately.

  - Waste handling, ventilation and processing plant

    - Items of plant deemed critical to the efficient and adequate processing of waste at the facility (including inter alia waste-loading vehicles and ejector trailers) shall be provided on the following basis:

      - 100% duty capacity;

      - 20% standby capacity available on a routine basis; and

      - Provision of contingency  arrangements  and/or backup  and spares in the case of breakdown  of critical equipment.

12

Environmental Protection Agency	Licence Reg  No  W0258-O1

    - Within three months from the date of grant of this licence, the licensee shall provide a report for the agreement of the Agency detailing the duty and standby capacity in tonnes per day, of all waste handling and  processing equipment to be used at the facility. These capacities shall be based on the licensed waste intake, as per Schedule A: Limitations, of this licence.

    - The quantity of waste to be accepted at the facility on a daily basis shall not exceed the duty capacity of the equipment at the facility. Any exceedance of this intake shall be treated as an incident.

  - Wastewater Treatment System

    - The licensee shall provide and maintain  a Wastewater  Treatment  plant  at the facility for the treatment of sanitary effluent arising on-site. Any waste water treatment system and percolation area shall satisfy the criteria set out in the Code of Practice Wastewater Treatment and Disposal Systems Serving Single 1-louses (p.e < 10), published  by  the  Environmental Protection Agency. The licensee shall provide evidence of compliance with this condition within  12 months of the date of grant of this licence.

    - A wash-down water collection system and storage tank shall be installed within six months of the date of grant of this licence. Wash down water from the recycling building stored in the on-site storage tank(s) shall be tankered off-site in fully enclosed road tankers to an agreed Wastewater Treatment Plant or alternative facility and disposed of there.

  - Timber and Construction & Demolition Waste Recovery Area(s)

    - Within six months of the date of grant of this licence, the timber and construction & demolition waste recovery area shall at a minimum comprise the following:

      - an impermeable concrete slab;

      - collection and disposal infrastructure for all run-off,

      - appropriate bunding to provide visual and noise screening;

      - appropriate   arrangements   on   operating   equipment   to   contain   and restrict dust emissions; and

      - containment of all stockpiles to minimise dust generation.

    - Only timber and construction & demolition waste shall be accepted at this area. Wastes that are capable of being recovered shall be  separated  and stored temporarily in this area in advance of being subjected to other recovery activities at the facility or transport off the facility.

  - Monitoring  Infrastructure Groundwater

Groundwater  monitoring  wells  shall  be  constructed  having  regard  to the  guidance given in the Agency’s landfill manual “Landfill Monitoring”.

  - Dust/Odour Control

    - Within twelve months of the date of grant of this licence, the licensee shall install and provide adequate measures for the control of odours and dust emissions, including  fugitive  dust emissions, from the  facility.  Installation of an odour and dust management system shall at a minimum include the following:

      - Dust curtains (or equivalent approved by the Agency) shall  be maintained on the entry/exit points from the waste transfer building; all other doors in this building shall be kept closed where possible.

13

Environmental Protection Agency	Licence Reg. No  W0258-O1

      - Unless otherwise agreed by the Agency, all buildings used for storing or processing putrescible waste shall be maintained at negative air pressure.

      - Provision of 100% duty capacity and 20% standby capacity, backups and spares must be provided for the air handling, ventilation and abatement plant.

  - Unless otherwise agreed by the Agency, and on foot of an assessment to be prepared within 20 months of the date of grant of this licence of the need for a biofilter or other air abatement equipment, the licensee shall provide and maintain, within 24 months of the date of grant of this licence, a biofilter or suitable alternative for the treatment of extracted air from buildings used for storing or processing putrescible waste.

  - The licensee shall provide and use adequate lighting during the operation  of the facility in hours of darkness.

  - The licensee shall establish and maintain, for each component of the facility, all infrastructure referred to in this licence in advance of the commencement of the licensed activities in that component, or as required by the conditions of this licence. Infrastructure specified in the application that relates to the environmental performance of the installation and is not specified in the licence, shall be installed in accordance with the schedule submitted in the application.

  - The licensee shall install on all emission points such sampling points or equipment, including any data-logging or other electronic communication equipment, as may be required by the Agency. All such equipment shall be consistent with the  safe operation of all sampling and monitoring systems.

  - In the case of composite sampling of aqueous emissions from the operation of the facility, a separate composite sample or homogeneous sub-sample (of sufficient volume as advised) shall be refrigerated immediately after collection and retained as required for EPA use.

3A8	The licensee shall clearly label and provide safe and permanent access to all on-site sampling and monitoring points and to off-site points as required by the Agency. The requirement with regard to off-site points is subject to the prior agreement of the landowner(s)  concerned.

  - Tank, Container and Drum Storage Areas

    - All tank, container and drum storage areas shall be rendered impervious to the materials stored therein. Bunds shall be designed having regard  to Agency guidelines ‘Storage and Transfer of Materials for Scheduled Activities’  (2004).

    - All tank and drum storage areas shall,  as a  minimum, be bunded, either locally or remotely, to a volume not less than the greater of the following:

    - 110% of the capacity of the largest tank or drum within the bunded area; or

    - 25% of the total volume of substance that could be stored within the bunded area.

    - All drainage from bunded areas shall be treated as hazardous waste unless it can be demonstrated to be otherwise. All drainage from bunded areas shall be diverted for collection and safe disposal.

    - All inlets, outlets, vent pipes, valves and gauges must be within the bunded area.

    - All tanks, containers and drums shall be labelled to clearly indicate their contents.

  - The licensee shall have in storage an adequate supply of containment booms and/or suitable absorbent material to contain and absorb any spillage at the facility. Once used, the absorbent material shall be disposed of at an appropriate facility.

14

Environmental Protection A2encv	Licence Reg  No. W0258-O1

  - Silt Traps and Oil Separators

The licensee shall maintain silt traps and oil separators at the facility:

- Silt traps to ensure that all storm water discharges, other than from roofs, from the facility pass through a silt trap in advance of discharge;

- An oil separator on the storm water discharge from yard areas. The separator shall be a Class I full retention separator.

The  silt  traps  and  separator  shall  be  in  accordance  with  I.S.  EN-858-2:  2003 (separator systems for light liquids).

  - Fire-water Retention

    - The licensee shall carry out a risk assessment to determine if the activity should have a fire-water retention facility. The licensee shall submit the assessment	and a report to the Agency on the findings and recommendations of the assessment within six months of the date of grant of this licence.

    - In the event that a significant risk exists for the release of contaminated fire- water, the licensee shall, based on the findings of the risk  assessment, prepare and implement, with the agreement of the Agency, a suitable risk management programme. The risk management programme shall be fully implemented within three months of date of notification by the Agency.

    - In the event of a fire or a spillage to storm water, the site storm water shall be diverted to the containment pond. The licensee shall examine, as part of the response programme in Condition 3.22.2 above, the provision of automatic diversion of storm water to the containment pond. The licenses shall have regard to any  guidelines issued by  the  Agency with regard to firewater retention.

    - The licensee shall have regard to the Environmental  Protection  Agency Draft Guidance Note to Industry on the Requirements for Fire-Water Retention Facilities when  implementing  Conditions  3.22.1  and  3.22.2 above.

  - All pumps sumps, storage tanks or other treatment plant chambers from  which spillage of environmentally significant materials  might  occur  in such quantities  as are likely to breach local or remote containment or separators, shall be fitted with high liquid level alarms (or oil detectors as appropriate) within six months from the date of grant of this licence.

  - The provision of a catchment system to collect any leaks from flanges and valves of all over-ground pipes used to transport material other than water shall be examined. This shall be incorporated into a Schedule of Environmental Objectives and Targets set out in Condition 2 of this licence for the reduction in fugitive emissions.

  - All wellheads, as shown on drawing number Ce07-253-Ol-204 Revision  A (GW3) and drawing number Ce07-253-01-208 Revision A  (GW1 & GW2) of the licence application shall be adequately protected to prevent contamination or  physical damage.

  - The licensee shall, within three months of the date of grant of this licence, install in a prominent location on the site a wind sock, or other wind direction indicator, which shall be visible from the public roadway outside the site. The licensee shall provide and maintain suitable infrastructure at the facility for the automated monitoring and recording of wind speed.

Reason:		To provide for  appropriate operation of the facility  to ensure protection  of the environment.

15

Environmental Protection Agency	Licence Re No  W0258-O1

## Condition 4.	Interpretation

  - Emission limit values for emissions to waters in this licence shall be interpreted in the following way:

    - Continuous Monitoring

      - No flow value shall exceed the specific limit.

      - No pH value shall deviate from the specified range.

      - No temperature value shall exceed the limit value.

    - Composite  Sampling

      - No pH value shall deviate from the specified range.

      - For parameters other than pH and flow, eight out of ten consecutive composite results, based on flow proportional  composite  sampling, shall not exceed the emission limit value. No individual results similarly calculated shall exceed  1.2 times the emission limit value.

    - Discrete Sampling

For parameters  other than pH and temperature,  no grab sample value shall exceed  1.2 times the emission limit value.

  - Where the ability to measure a parameter is affected  by  mixing  before  emission, then, with agreement from the Agency, the parameter may be assessed before mixing takes place.

  - Noise

Noise from the facility shall not give rise to sound pressure levels (Leq, T) measured at the noise sensitive locations of the facility which exceed the limit value(s).

  - Dust and Particulate Matter

Dust and particulate matters from the activity shall not give rise to deposition  levels which exceed the limit value(s).

Reason:	To clarify the interpretation of limit values fixed  under the licence.

Condition 5.	Emissions

5.1	No specified emission from the facility shall exceed the emission limit values set out in Schedule B: Emission Limits, of this licence. There shall be no other emissions of environmental  significance.

5.2	No emissions, including odours, from the activities carried on at the site shall result in an impairment of, or an interference with amenities or the environment beyond the facility boundary or any other legitimate uses of the environment beyond the facility boundary.

  - No substance shall be discharged in a manner, or at a concentration, that, following initial dilution, causes tainting of fish or shellfish.

  - The licensee shall ensure that all or any of the following:

    - Vermin

    - Birds

    - Flies

    - Mud Dust

16

Environmental Protection Agency	Licence Re2 No  W0258-O1

Litter

associated with the activity do not result in an impairment of, or an interference with, amenities or the environment at the facility or beyond the facility boundary or any other legitimate uses of the environment beyond the facility boundary. Any method used by the licensee to control or prevent any such impairmentlinterference shall not cause environmental  pollution.

5.5		Unless otherwise agreed by the Agency, no trade effluent, leachate and/or contaminated storm water shall be discharged to surface water drains  and  surface water courses.

5.6	There shall be no direct emissions to groundwater.

Reason:		To provide for  the protection  of the environment by way of control and limitation of emissions.

Condition 6.	Control and Monitoring

  - Test Programme

6.1. 1 The licensee shall  prepare to the satisfaction of the  Agency,  a  test programme for abatement equipment installed to abate emissions to atmosphere.  This programme  shall be submitted to the Agency in advance of implementation.

    - The programme, following agreement by the Agency, shall be completed within three months of the commencement of operation of the abatement equipment.

    - The criteria for the operation of the abatement equipment as determined by the test programme, shall be incorporated into the standard operating procedures.

    - The test programme shall as a minimum:

      - establish all criteria for operation, control and management of the abatement equipment to ensure compliance with the emission limit values specified in this licence; and

      - assess the performance of any monitors on the abatement system and establish a maintenance and calibration programme for each monitor.

    - A report on the test programme shall be submitted to the Agency within one month of completion.

  - The licensee shall carry out such sampling, analyses, measurements, examinations, maintenance and calibrations as set out below and as in accordance with Schedule C: Control & Monitoring, of this licence.

    - Analyses shall be undertaken by competent staff in accordance with documented operating procedures.

    - Such procedures shall be assessed for their suitability for the test matrix and performance  characteristics  shall be determined.

    - Such procedures shall be subject to a programme of Analytical Quality Control using control standards with evaluation of test responses.

    - Where any analysis is sub-contracted it shall be to a competent laboratory.

  - The licensee shall ensure that:

    - sampling and analysis for all parameters listed in the Schedules to this licence; and

17

Environmental Protection Aencv	Licence Reg. No  W0258-OI

    - any reference  measurements  for the calibration  of automated  measurement systems;

shall be carried out in accordance with CEN-standards. If CEN standards are not available, ISO, national or international standards that will ensure the provision of data of an equivalent scientific quality shall apply.

  - All automatic monitors and samplers shall be functioning at all times (except during maintenance and calibration) when the activity is being carried on unless alternative sampling or monitoring has been agreed in writing by the  Agency  for  a  limited period. In the event of the malfunction of any continuous monitor, the licensee shall contact the Agency as soon as practicable, and alternative sampling and monitoring facilities shall be put in place. The use of alternative equipment, other than in emergency situations, shall be as agreed by the Agency.

  - Monitoring and analysis equipment shall be operated and maintained as necessary so that monitoring accurately reflects the emissionldischarge (or ambient conditions where that is the monitoring objective).

  - The licensee shall ensure that groundwater monitoring well sampling equipment is available/installed on-site and is fit for purpose at all times. The sampling equipment shall be to Agency specifications.

  - All treatment/abatement and emission control equipment shall be calibrated and maintained in accordance with the  instructions  issued  by the manufacturer/supplier or installer.

  - The frequency, methods and scope of monitoring, sampling and analyses, as set out in this licence, may be amended with the agreement of the Agency following evaluation of test results.

  - The licensee shall prepare a programme, to the satisfaction of the Agency, for the identification and reduction  of fugitive emissions using an appropriate combination of best available techniques. This programme shall  be  included  in  the Environmental  Management Programme.

  - The integrity and water tightness of all underground pipes, tanks, bunding structures and containers and their resistance to penetration by water or other materials carried or stored therein shall be tested and demonstrated by the licensee within six months of the date of grant of this licence. This testing shall be carried out by the licensee at least once every three years thereafter and reported to the Agency on each occasion. This testing shall be carried out in accordance with  any guidance published by the Agency. A written record of all  integrity  tests  and  any  maintenance  or remedial work arising from them shall be maintained by the licensee.

  - The drainage system (i.e., gullies, manholes, any visible drainage conduits and such other aspects as may be agreed) and bunds, silt traps and oil separators shall be inspected weekly and desludged as necessary. All sludge and drainage from these operations shall be collected for safe disposal. The drainage system, bunds, silt traps and oil interceptors shall be properly maintained at all times.

  - An inspection for leaks on all flanges and valves on over-ground pipes used to transport materials other than water shall be carried out weekly. A log of such inspections shall be maintained.

  - Storm Water

A visual examination of the storm water discharges shall be carried out daily. A log of such inspections shall be maintained.

18

Environmental Protection Aencp	Licence Re2  No  W0258-O1

6.14	Ground Water

The licensee shall, as required by the Agency, arrange for the carrying out, by an appropriately qualified consultantJprofessional, of a comprehensive hydrogeological investigation of the site. The scope, detail and programme,  including report structure and reporting schedule, for this investigation must be agreed by the Agency prior to implementation. Any recommendations arising from a report or reports on this investigation must be implemented within such a period to be agreed by the Agency.

  - Noise

The licensee shall carry out a noise survey  of the  site  operations  annually.  The survey programme shall be undertaken in accordance with the methodology specified in the ‘Environmental Noise Survey Guidance Document’ as published by the Agency.

  - Pollutant Release and Transfer Register (PRTR)

The licensee shall prepare and report a PRTR for the site. The  substance  andlor wastes to be included in the PRTR shall be as agreed by the Agency each year by reference to EC Regulations No. 166/2006 concerning the establishment of the European Pollutant Release and Transfer Register. The PRTR shall be prepared in accordance with any relevant guidelines issued by the Agency and shall be submitted electronically in specified format and as part of the AER.

6. 17 The licensee shall, within six months of the date of grant of this licence, develop and estabHsh a Data Management System for collation, archiving,  assessing  and graphically presenting the monitoring data generated as a result of this licence.

  - Litter Control

    - All loose  litter or other waste, placed on or in the vicinity of the facility, other than in accordance with the requirements of this licence, shall be removed, subject to the agreement of the landowners, immediately  and  in any event by 10.00 am of the next working day after such waste is discovered.

    - The licensee shall ensure that all vehicles delivering waste to and removing waste and materials from the facility are appropriately covered.

  - Dust/Odour Control

    - All putrescible waste, mixed municipal waste and waste for disposal stored overnight at the facility shall be stored in suitably covered and enclosed containers, and shall be removed from the facility within 48 hours, except at Public Holiday weekends. At Public Holiday weekends, waste for disposal shall be removed within 72 hours of its arrival on site.

    - In dry weather, site roads and any other areas used by vehicles or for storing potentially dusty waste shall be sprayed with water as and when required to minimise airborne dust nuisance.

    - The licensee shall undertake, within six months of the date of grant of this licence, an odour assessment which shall include as a minimum the identification and quantification of all significant odour sources and an assessment of the suitability and adequacy of the odour abatement system(s) to deal with these emissions. Any recommendations arising from  such an odour assessment shall be implemented following agreement with the Agency.

  - Operational  Controls

    - The floor of the waste transfer building shall be cleaned on a weekly basis and on a daily basis where putrescible waste is handled. The floor of the storage bays for recovered wastes shall  be washed down and  cleaned  on each occasion such bays are emptied, or as a minimum on a weekly basis.

    - Scavenging shall not be permitted at the facility.

19

Environmental Protection Agency	Licence Reg  No  W0258-OI

    - All tanks and drums shall be labelled to clearly indicate their contents.

    - There shall be no unauthorised public access to the facility.

    - The wood  shredder, the C&D waste crusher  and the C&D waste  screener shall not be operated when wind speeds exceed  10.7 mIs (Force 5).

  - Monitoring Locations

Within three months of the date of grant of this licence, the licensee shall submit to the Agency an appropriately scaled drawing(s) showing all the monitoring locations that are stipulated in this licence including any noise-sensitive locations and private wells to be monitored. The drawing shall include the eight-digit national grid reference of each monitoring point.

  - Nuisance Monitoring

The licensee shall daily inspect the facility and its immediate surrounds for nuisances caused by litter, vermin, birds, flies, mud, dust and odours. The licensee shall maintain a record of all nuisance inspections.

Reason:  To provide for  the protection  of the environment by vay of treatment and monitoring  of emissions.

Condition 7.	Resource Use and Energy Efficiency

  - The licensee shall carry out an audit of the energy efficiency of the site within one year of the date of grant of this licence. The audit shall be carried out in accordance with the guidance published by the Agency, “Guidance Note on Energy Efficiency Auditing”. The energy efficiency audit shall be repeated at intervals as required by the Agency.

  - The audit shall identify all practicable opportunities for energy use reduction and efficiency and the recommendations of the audit will be incorporated into the Schedule of Environmental Objectives and Targets under Condition 2 above.

  - The licensee shall identify opportunities  for reduction in the quantity of water used on site including recycling and reuse initiatives, wherever possible. Reductions in water usage shall be incorporated into Schedule of Environmental Objectives and Targets.

  - The licensee shall undertake an assessment of the efficiency of use of raw materials in all processes, having particular regard to the reduction in waste generated. The assessment should take account of best international practice for this type of activity. Where improvements are identified, these shall be incorporated into the Schedule of Environmental  Objectives and Targets.

Reason:	To provide for  the efficient use of resources and energy in all site operations.

Condition 8.	Materials  Handling

  - With the exception of wood shredding and the  screening  and  crushing  of construction and demolition waste, all waste processing  shall be carried  out inside the waste transfer buildings.

20

Environmental Protection A.gency	Licence Reg  No  W0258-O1

  - Only non-putrescible waste shall be stored outdoors. Mechanically recovered marketable waste produced at the facility may be stored outdoors only under conditions that will not diminish the integrity or value of the recovered waste or lead to nuisance emissions including dust and odour. All such storage areas shall  be covered except as may be agreed by the Agency.

  - Waste Acceptance and Characterisation  Procedures

    - Waste shall only be accepted at the facility from Local Authority waste collection or transport vehicles or holders of waste collection  permits, unless exempted or excluded, issued under the  Waste  Management  Acts 1996 to 2011.  Copies of these waste collection permits must be maintained at the facility.

    - Within six months of the date  of grant of this licence, the licensee shall establish and maintain detailed written procedures for the acceptance and handling of waste.

    - Waste shall be accepted at the facility only from known customers or new customers subject to initiaL waste profiling and waste characterisation off- site. The written records of this off-site waste profiling and characterisation shall be retained by the licensee for all active customers and for a two year period following termination  of licensee/customer  agreements.

    - Waste arriving  at the facility shall have its documentation checked  at the point of entry to the facility and subject to this verification, weighed, documented and directed to the Waste Transfer  Building.  Each  load  of waste arriving at the Waste Transfer Building shall be inspected  upon tipping within this building. Only after such inspections shall the waste be processed for disposal or recovery.

8.3.5	Any waste deemed unsuitable for processing at the facility and/or in contravention of this licence shall be immediately separated and  removed from the facility at the earliest possible time. Temporary storage of such wastes shall be in a designated Waste Quarantine Area.  Waste  shall  be stored under appropriate conditions in the quarantine area to avoid putrefaction, odour generation, the attraction of vermin and any other nuisance or objectionable condition.

  - Recovery of waste on-site shall only take place in accordance with the conditions of this licence and in accordance with  the  appropriate  National  and  European legislation and protocols.

  - Waste sent off-site for recovery or disposal shall be transported only by an authorised waste contractor. The waste shall be transported from  the  site of the activity to the site of recovery/disposal only in a manner that  will  not  adversely affect the environment and in accordance with the  appropriate   National  and European legislation and protocols.

  - The licensee shall ensure that, in advance of transfer to another person, waste shall be classified, packaged  and labelled in accordance with National, European and any other standards which are in force in relation to such labelling.

  - The loading and unloading of materials shall be carried out in designated areas protected against spillage and leachate run-off.

  - Waste shall be stored in designated areas, protected as may be appropriate against spillage and leachate run-off. The waste shall be clearly labelled and appropriately segregated.

  - No waste classified as green list waste in accordance with the EU Shipment of Waste Regulations (Council Regulation EEC No. 1013/2006, as may be amended) shall be consigned for recovery without the agreement of the Agency.

  - Waste for disposal/recovery off-site shall be analysed in accordance  with Schedule C: Control & Monitoring, of this licence.

21

Environmental Protection A.ency	Licence Reg  No  W0258-O1

  - Unless approved in writing, in  advance, by the Agency the  licensee  is prohibited from mixing a hazardous waste of one category with a hazardous waste of another category or with any other non-hazardous waste.

  - The licensee shall neither import  waste into the State nor  export waste out of the State except in accordance with the relevant provisions of Regulation (EC) No 1013/2006 of the European Parliament and of the Council of 14th June 2006 on shipments of waste and associated national regulations.

  - No separately collected waste or recovered fraction of waste shall be  mixed  with waste of different characteristics or properties or dispatched for disposal at another facility unless agreed by the Agency.

Reason:		To pro videfor  the appropriate handling of material and the protection  of the environment.

Condition 9.	Accident Prevention and Emergency

Response

  - The licensee  shall, within six months of date of grant of this licence, ensure that a documented Accident Prevention Procedure is in place that addresses the hazards on- site, particularly in relation to the prevention of accidents with a possible impact on the environment. This procedure shall be reviewed annually and updated  as necessary.

  - The licensee shall, within six months of date of grant of this licence, ensure that a documented Emergency Response Procedure is in place, that  addresses  any emergency situation which may originate on-site. This procedure shall include provision for minimising the effects of any emergency on the environment. This procedure shall be reviewed annually and updated as necessary.

  - Incidents

    - In the event ofan incident the licensee shall immediately:

      - carry out an investigation to identify the nature, source and cause of the incident and any emission arising therefrom;

      - isolate the source of any such emission;

      - evaluate   the   environmental   pollution,   if   any,   caused   by   the incident;

      - identify	and	execute	measures	to	minimise	the emissions/malfunction  and the effects thereof;

      - identify the date, time and place of the incident;

      - notify the Agency and other relevant authorities.

    - The licensee shall provide a proposal to the Agency for its agreement within one month of the incident occurring or as otherwise agreed by the Agency, to:

      - identify and put in place measures to avoid recurrence of the incident; and

      - identify and put in place any other appropriate remedial actions.

22

Environmental Protection Apencp	Licence Reg  No  W0258-OI

  - Emergencies

    - In the event of a breakdown of equipment or any other occurrence which results in the closure of the transfer station building, any waste arriving at or already collected at the facility  shall be transferred directly  to appropriate landfill sites or any other appropriate facility until such time as the transfer station building is returned to a fully operational status. Such a breakdown event will be treated as an emergency and rectified as soon as possible.

    - All significant spillages occurring at the facility shall be treated as an emergency and immediately cleaned up and dealt  with  so as to  alleviate their effects.

    - No waste shall be burnt within the boundaries of the facility. A fire at the facility shall be treated as an emergency and immediate action shall be taken to extinguish it and notify the appropriate authorities.

    - In the event that monitoring of local wells indicates that  the  facility  is having a significant adverse effect on the quantity  andlor  quality  of  the water supply this shall be treated as an emergency and the licensee shall provide an alternative supply of water to those affected.

Reason:	Toprovide for  the protection  of the environment.

Condition 10.	Closure, Restoration  and Aftercare

Management

  - Following termination, or planned cessation for a period greater than six months, of use or involvement of all or part of the site in the licensed activity, the licensee shall, to the satisfaction of the Agency, decommission, render safe or remove for disposallrecovery any soil, subsoil, buildings, plant or equipment, or any waste, materials or substances or other matter contained therein or thereon, that may result in environmental pollution.

  - Decommissioning  Management  Plan (DMP)

    - The licensee shall prepare, to the satisfaction of the Agency, a fully detailed and costed plan for the decommissioning or closure of the site or  part thereof. This plan shall be submitted to the Agency  for agreement  within six months of the date of grant of the licence.

    - The plan shall be reviewed annually and proposed amendments thereto notified to the Agency for agreement as part of the AER. No amendments may be implemented without the agreement of the Agency.

    - The licensee shall have regard to the Environmental Protection Agency Guidance	on Environmental Liability Risk Assessment, Residuals Management Plans and Financial Provision when implementing Condition

10.2.1 above.

  - The   Decommissioning    Management   Plan   shall   include,   as   a   minimum,   the following:

- a scope statement for the plan;

- the criteria that define the successful decommissioning  of the activity or part thereof, which ensures minimum impact on the environment;

- a programme to achieve the stated criteria;

- where	relevant,	a	test	programme	to	demonstrate	the	successful implementation of the decommissioning plan; and

23

Environmental Protection A2encv	Licence Reg  No  W0258-O1

- details of the costings for the plan and the financial provisions to underwrite those costs.

  - A final validation report to include a certificate of completion for the Decommissioning Management Plan, for all or part of the site as necessary, shall be submitted to the Agency within three months of execution of the plan. The licensee shall carry out such tests, investigations or submit certification, as requested by the Agency, to confirm that there is no continuing risk to the environment.

Reason:		To make provision for the proper  closure of the activity ensuring protection  of the environment.

Condition 11.	Notification, Records and Reports

  - The licence shall notify the Agency by both telephone and facsimile, if available, to the Agency’s headquarters in Wexford, or to such other Agency office as may be specified by the Agency, as soon as practicable after the occurrence of any of the following:

    - any release of environmental significance to atmosphere from any potential emissions point including bypasses;

    - any emission that does not comply with the requirements of this licence;

    - any malfunction or breakdown of key control equipment or monitoring equipment set out in Schedule C: Control and Monitoring, of this licence which is likely to lead to loss of control of the abatement system; and

    - any incident with the potential for environmental contamination of surface water or groundwater, or posing an environment threat to air or land, or requiring an emergency response by the Local Authority.

The licensee shall include as part of the notification, date and time of the incident, summary details of the occurrence, and where available, the steps taken to minimise any emissions.

  - In the event of any incident which relates to discharges to sewer having taken place, the licensee shall notify the Local and Water Services Authority as soon as practicable after such an incident.

  - In the case of any incident relating to discharges to water, the licensee shall notify the Local and Water Services Authority and Inland Fisheries Ireland as soon as practicable after such an incident.

II .4     The licensee shall make a record of any incident.  This record shall include details of the nature, extent, and impact of, and circumstances giving rise to, the incident. The record shall include all corrective actions taken to manage the incident, minimise wastes generated and the effect on the environment, and avoid  recurrence.  The licensee shall, as soon as practicable following incident notification, submit to the Agency the incident record.

  - The licensee shall record all complaints of an environmental nature related to the operation of the activity. Each such record shall give details of the date and time of the complaint, the name of the complainant (if provided), and give  details  of the nature of the complaint. A record shall also be kept of the response made in the case of each complaint.

  - The licensee shall record all sampling, analyses, measurements, examinations, calibrations and maintenance carried out in accordance with the requirements of this licence and all other such monitoring which reLates to  the  environmental performance of the facility.

24

Environmental Protection Agenci’	Licence Reg  No  W0258-O1

  - The licensee shall as a minimum keep the following documents at the site:

    - the licences relating to the facility;

    - the current EMS for the facility;

    - the previous year’s AER for the facility;

    - records of all sampling, analyses, measurements, examinations, calibrations and maintenance carried out in accordance with the requirements of this licence and all  other such monitoring which relates to the environmental performance of the facility;

    - relevant correspondence with the Agency;

    - up-to-date site drawings/plans showing the location of key process and environmental infrastructure, including monitoring locations and emission points;

    - up-to-date Standard Operational Procedures for all processes, plant and equipment necessary to give effect to this licence or otherwise to ensure that standard operation of such processes, plant or equipment does not result in unauthorised emissions to the environment; and

    - any elements of the licence application referenced in this licence.

This documentation shall be available to the Agency for inspection at all reasonable times.

  - The licensee shall submit to the Agency,  by the 3 jst March of each year, an AER covering the previous calendar year. This report, which shall be to the satisfaction of the Agency, shall include as a minimum the information specified in Schedule F: Annual Environmental Report, of this  licence  and shall be prepared in accordance with any relevant guidelines issued by the Agency.

  - A full record, which shall be open to inspection by authorised persons of the Agency at all times, shall be kept by the licensee on matters  relating to the waste management operations and practices at this site.  This record shall be maintained on a monthly basis and shall as a minimum contain details of the following:

    - the tonnages and EWC Code for the waste materials imported andlor sent off-site for disposal/recovery;

    - the names of the agent and carrier of the waste, and their waste collection permit details, if required (to include issuing authority and  vehicle registration number);

    - details of the ultimate disposal/recovery destination  facility  for the  waste and its appropriateness to accept the consigned waste stream, to include its permitllicence details and issuing authority, if required;

    - written confirmation of the acceptance and disposal/recovery of any hazardous waste consignments sent off-site;

    - details of all waste consigned abroad for Recovery and classified as ‘Green’ in accordance with the EU Shipment of Waste Regulations (Council Regulation EEC No. 1013/2006, as may be amended). The rationale for the classification must form part of the record;

    - details of any rejected consignments;

    - details of any approved waste mixing;

    - the results of any waste analyses required under Schedule C: Control & Monitoring, of this licence; and

    - the tonnage and EWC Code for the waste materials recoveredldisposed on­ site.

  - The licensee shall submit report(s) as required by the conditions of this licence to the Agency’s Headquarters in Wexford, or to such other Agency office as may be specified by the Agency.

25

  - All reports shall be certified accurate and representative by the facility manager or a nominated, suitably qualified and experienced deputy.

  - A record shall be kept of each consignment of trade effluent, leachate andlor contaminated storm water removed from the facility. The record shall include the following:

(1)	the name of the carrier;

- the date and time of removal  of trade  effluent, leachate andlor contaminated storm water  from the facility;

- the  volume  of trade  effluent,  leachate  and/or  contaminated  storm  water,  in cubic metres, removed from the facility on each occasion;

- the name and address of the Wastewater  Treatment Plant to which the trade effluent, leachate andlor contaminated storm water was transported; and

- any incidents or spillages of trade effluent, leachate andlor contaminated storm water during its removal or transportation.

  - Waste Recovery Reports

The licensee shall as part of the Annual Environmental Report for the site submit a report on the contribution by this facility to the achievement of the waste recovery objectives stated in Condition 2.2.2.2 and as otherwise may be stated in National and European Union waste policies and shall, as a minimum, include the following:

    - the recovery of metals;

    - the recovery of C & D derived waste materials;

    - the recovery/treatment of biowaste (including contribution of facility to the pre-treatment targets in the EU Landfill Directive);

    - the separation and recovery of other recyclable materials.

Reason:		To provide for  the collection and reporting of adequate information on the activity.

Condition 12.	Financial Charges and Provisions

  - Agency Charges

    - The licensee  shall pay to the Agency an annual contribution of €9,767, or such sum as the Agency from time to time determines, having regard to variations in the extent of reporting, auditing, inspection, sampling and analysis or other functions carried out by the Agency, towards the cost of monitoring the activity as the Agency considers necessary for the performance of its functions under the Waste Management  Acts  1996 to 2011. The first payment shall be a pro-rata amount for the period from the date of grant of this licence to the 3l day of December, and shall be paid to the Agency within one  month from  the date of grant of the licence. In subsequent years the licensee shall pay to the Agency such revised  annual contribution as the Agency shall  from time to time consider necessary to enable performance by the Agency of its relevant functions under the Waste Management Acts 1996 to 2011, and all such payments shall  be  made within one month of the date upon which demanded by the Agency.

    - In the event that the frequency or extent of monitoring or other functions carried out by the Agency needs to be increased, the licensee  shall contribute such sums as determined by the Agency to defray its costs in regard to items not covered by the said annual contribution.

26

  - Environmental  Liabilities

    - The licensee shall as part of the AER, provide an annual statement as to the measures taken or adopted at the site in relation to the prevention of environmental damage, and the financial provisions in place in relation to the underwriting of costs for remedial actions following anticipated events (including closure) or accidents/incidents, as may be associated with the carrying on of the activity.

    - The licensee shall arrange for the completion, by an independent and appropriate qualified consultant, of a comprehensive and fully costed Environmental Liabilities Risk Assessment (ELRA) which addresses the liabilities from past and present  activities.  The  assessment  shall  include those liabilities and costs identified in Condition 10 for execution of the DMP. A report on this assessment shall be submitted to the Agency for agreement within six months of date of grant of this licence. The ELRA shall be reviewed as necessary to reflect any significant change on site, and in any case every three years following initial agreement. Review results are to be notified as part of the AER.

    - As part of the measures identified in Condition 12.2.1, the licensee shall, to the satisfaction of the Agency, make financial provision to cover any liabilities associated with the operation (including closure, restoration and aftercare). The amount of indemnity held shall be reviewed and revised as necessary, but at least annually. Proof of renewal or revision of  such financial indemnity shall be included in the annual ‘Statement of Measures’ report identified in Condition  12.2.1.

    - The licensee shall revise the cost of closure, restoration and aftercare annually and any adjustments shall be reflected in the financial provision made under Condition  12.2.3.

    - The licensee shall have regard to the Environmental Protection Agency Guidance	on Environmental Liability Risk Assessment, Residuals Management Plans and Financial  Provision when implementing Conditions

12.2.2 and 12.2.3 above.

Reason:		To pro videfor  adequate financing for  monitoring andfinancial  provisions for measures to protect  the environment.

27

SCHEDULE A:	Limitations

  - Limitations on thefacility

The following waste related processes are authorised:

    - Sorting, shredding, crushing, baling, repackaging processes

    - C&D waste recovery processes (md. crushing, screening, sorting, blending)

- Storage of waste

No additions to these processes are permitted unless agreed in advance with the Agency.

  - Waste Acceptance

Table A.2 Waste Categories and Quantities

Note 1:	Any proposals to accept other compatible non-hazardous waste types shall be agreed in advance by the Agency.

Note 2:	The limitation on individual non-hazardous waste types may be varied with the agreement of the Agency subject to the total limit for non-hazardous waste staying the same.

28

SCHEDULE B:	Emission Limits

  - Emissions to Air

There shall be no emissions to air of environmental significance.

  - Emissions to Water

There shall be no emissions to water of environmental significance.

  - Emissions to Sewer

There shall be no process effluent emissions to sewer.

  - Noise Emissions

| Daytime dB(A) LAe0 (30 minutes) | Night-time dB(A) LAe0 (30 minutes) |
| --- | --- |
| Note I | Note I |

Note 1:	There shall be no clearly audible tonal component or impulsive component in the noise emission from the

activity of any noise-sensitive location.

  - Ambient Air Limits

Dust Deposition Limits:

| Parameter | Level (mg/rn2 per day) Note I |
| --- | --- |
| Total dust deposition | 350 |

Note 1:	30 day composite sample with the results expressed as mg/m’ per day.

  - Storm Water Emissions

| Parameter | Level (mg/I) |
| --- | --- |
| Suspended Solids | 35 |
| COD | 40 |

29

###### SCHEDULE C:	Control & Monitoring

C.1.1	Control of Emissions to Air

There shall be no emissions to air of environmental significance.

C.1.2   Monitoring of Emissions to Air

There shall be no emissions to air of environmental significance.

    - Control of Emissions to Water

There shall be no emissions to water of environmental significance.

    - Monitoring of Emissions to Water

There shall be no emissions to water of environmental significance.

    - Monitoring of Storm Water Emissions

Emission Point Reference No:	SW3 (303856, 148583)

| Parameter | Monitoring Frequency Note I | Analysis Method/Technique |
| --- | --- | --- |
| Visual Inspection | Daily | Sample and examine for colour and |
|  |  | odour |
| pH | Weekly | Standard method |
| Temperature | Weekly | Standard method |
| COD | Quarterly | Standard method |
| Total Ammonia | Quarterly | Standard method |
| Total Nitrogen | Quarterly | Standard method |
| Conductivity | Quarterly | Standard method |
| Faecal coliforms | Quarterly | Standard method |
| Total coliforms | Quarterly | Standard method |
| Suspended Solids | Quarterly | Standard method |
| Mineral Oils | Quarterly | Standard method |

Note 1: Grab Sample.

30

    - Control of Emissions to Sewer

There shall be no process effluent emissions to sewer.

    - Monitoring of Emissions to Sewer

There shall be no process effluent emissions to sewer.

  - Waste Monitoring

| Waste Class | Frequency | Parameter | Method |
| --- | --- | --- | --- |
| Other Note I |  |  |  |

Note 1:	Analytical requirements to be determined on a case by case basis.

  - Noise Monitoring

Monitoring Point Locations:	NS1 (304153,  148680)

NS2 (303882,  148589)

| Parameter | Monitoring Frequency | Analysis Method/Technique |
| --- | --- | --- |
| L(A)EQ [30 minutesl L(A)10 [30 minutesl L(A)90 [30 minutesl Frequency analysis (1/3 octave band analysis) | Annual Annual Annual Annual | Standard Note I Standard Note I Standard Note I Standard N0te I |

Note 1:  “International Standards Organisation. ISO 1996. Acoustics - Description and Measurement of

Environmental Noise. Parts 1,2 and 3.”

  - Ambient Monitoring

C.6.1  Dust Monitoring

Location:	Dl (303889, 148561)

D2 (304115, 148666)

| Parameter | Monitoring Frequency | Analysis Method/Technique |
| --- | --- | --- |
| Dust deposition | Quarterly | Bergerhoff |

31

C.6.2	Groundwater Monitoring

Location:	GW1 (304036E, 148689N) GW2 (303865E, 148542N)

GW3 (located near the facility entrance)

| Parameter | Monitoring Frequency | Analysis Method/Techniques |
| --- | --- | --- |
| pit | Biannually | pH electrode/meter |
| COD | Biannually | Standard Method |
| Nitrate | Biannually | Standard Method |
| Total Ammonia | Biannually | Standard Method |
| Total Nitrogen | Biannually | Standard Method |
| Conductivity | Biannually | Standard Method |
| Chloride | Biannually | Standard Method |
| Fluoride | Biannually | Standard Method |
| Organic Compounds Notel | Biannually | Standard Method |
| Faecal coliforms | Biannually | Standard Method |
| Total coliforms | Biannually | Standard Method |

Note 1:	Screening for pollutant list substances (such as US EPA volatile and/or semi-volatile compounds).

##### SCHEDULE D:	Specified Engineering Works

Specified Engineering Works

Development of the facility including installation of waste-handling, processing, recycling/recovery  infrastructure and

installation of increased waste processing capacity as well as any pollution  abatement system(s).

Installation of storm water drainage network including silt traps and oil interceptors. Installation of dust/odour control and abatement system(s).

Installation of a wash down water collection system and storage tank. Any other works notified in writing by the Agency.

32

SCHEDULE F:	Annual Environmental Report

Annual Environmental  Report Content Note 1

Waste activities carried out at the facility.

Quantity and composition of waste recovered, received and disposed of during the reporting period and each previous year (relevant EWC codes to be used).

Full title and a written summary of any procedures developed by the licensee in the year which relates to the facility operation.

Waste Recovery Report. Review of nuisance controls.

Volume of contaminated storm/wash water produced and volume transported off-site.

Emissions from the facility. Waste management record. Resource consumption  summary. Complaints  summary.

Schedule of Environmental  Objectives and Targets.

Environmental management programme — report for previous year. Environmental management programme — proposal for current year. Pollutant Release and Transfer Register — report for previous year. Pollutant Release and transfer Register — proposal for current year. Noise monitoring report summary.

Ambient monitoring summary.

Tank and pipeline testing and inspection report. Reported  incidents summary.

Energy efficiency audit report summary.

Report  on  the assessment of the efficiency  of use  of raw  materials  in processes  and the reduction  in waste generated.

Report on progress made and proposals being developed  to minimise water demand and the volume of trade effluent discharges.

Developmentllnfrastructural  works summary (completed in previous year or prepared  for current year). Reports on financial provision made under this licence, management and staffing structure of the facility,

and a programme  for public information.

Closure, restoration & aftercare management plan.

Statement  of  measures   in  relation   to  prevention   of  environmental   damage   and   remedial   actions (Environmental  Liabilities).

Environmental  Liabilities Risk Assessment Review (every three years or more frequently as dictated by relevant on-site change including financial provisions.

Any other items specified by the Agency.

Note 1:	Content may be revised subject to the agreement of the Agency.

Sealed by the seal of the Agency on this the 11th day of July 2012.

PRESENT when the seal of the Agency Was affixed hereto:

Dr.-Taren Creed, Authorised Person

33

# Text boxes

| Waste Type | Maximum Note 2 (Tonnes Per Annum) |
| --- | --- |
| Non- Hazardous Wastes Note I | Mixed Dry Recyclables | 4,800 |
|  | Source Separated Recyclables | 5,780 |
|  | Source Separated Bio-waste | 1,680 |
|  | Municipal Solid Waste | 7,200 |
|  | Construction & Demolition Waste | 5,040 |
| Non-Hazardous Waste Total | 24,500 |